## Slide 1: Datapath Design in RISC-V (R and I format Instructions)
Sparsh Mittal
Slide courtesy: Dr Garcia (UC Berkeley)

## Slide 2: Background topics

## Slide 3: Reminder from Digital Logic Course
Use muxes to select among input
  S input bits selects 2S inputs
  Each input can be n-bits wide, indep of S
Can implement muxes hierarchically
ALU can be implemented using a mux
  Coupled with basic block elements
N-bit adder-subtractor done using N 1-bit adders with XOR gates on input
  XOR serves as conditional inverter

## Slide 4: MUX
2:1 MUX
2n:1 MUX
4:1 MUX

## Slide 5: Multi-bit MUX

## Slide 6: Three-to-eight-line decoder

## Slide 7: Shifter
An N-bit shifter can be built from N N:1 multiplexers.
The input is shifted by 0 to N-1 bits, depending on the value of the log2N-bit select lines.

## Slide 9: ALU design using MUX
The circuit functionality of a 1 bit ALU is shown here, depending upon the control signal S1 and S0 the circuit operates as follows:
S1 = 0 , S0 = 0, the output is A And B,
S1 = 0 , S0 = 1, the output is A Or B,
S1 = 1 , S0 = 0, the output is A Xor B,
S1 = 1 , S0 = 1, the output is A Add B.

## Slide 10: ALU Design using MUX
0
1
2
3
3-bit adder
4
4:1 MUX with 6-bit selection
A
B
0
0
3-bit subtractor
4
A
B
0
0
3-bit subtractor
4
B
A
0
0
3-bit multiplier
6
B
A
6
M1
M2

## Slide 11: Single circuit for add and subtractor
The mode input M controls the operation.
M = 0, circuit is adder
M = 1  subtractor.
M = 1  B ⊕1 = B’ and C0 = 1.  B inputs are all complemented and a 1 is added through the input carry.
V= for overflow detection
Four-bit adder–subtractor (with overflow detection)

## Slide 12: Our Single-Core Computer so far…
Processor
Control
Datapath
PC
Registers
Arithmetic & Logic Unit
(ALU)
Memory
Input
Output
Bytes
Enable?
Read/Write
Address
Write Data
ReadData
Processor-Memory Interface
I/O-Memory Interfaces
Program
Data
Processor organized around words and bytes
Memory (including
cache) organized around blocks, which are typically multiple words

## Slide 13: The CPU
Processor (CPU): the active part of the computer that does all the work (data manipulation and decision-making)
Datapath: portion of the processor that contains hardware necessary to perform operations required by the processor
Control: portion of the processor (also in hardware) that tells the datapath what needs to be done

## Slide 14: Building a RISC-V Processor
Notes: Main point here is to give you an idea of why you won’t be allowed to do certain things in design
All boil down to making sure the chip you get back behaves the way you expected
  If don’t follow the rules, fab won’t guarantee functionality

## Slide 15: One-Instruction-Per-Cycle RISC-V Machine
On every tick of the clock, the computer executes one instruction
Current state outputs drive the inputs to the combinational logic, whose outputs settles at the values of the state before the next clock edge
At the rising clock edge, all the state elements are updated with the combinational logic outputs, and execution moves to the next clock cycle
Reg[]
pc
IMEM
DMEM
Combinational Logic
clock

## Slide 16: State Required by RISC-V32 “I” (Integer) ISA
Each instruction reads and updates this state during execution:
Registers (x0..x31)
  Register file (regfile) Reg holds 32 registers x 32 bits/register: Reg[0]..Reg[31]
  First register read specified by rs1 field in instruction
  Second register read specified by rs2 field in instruction
  Write register (destination) specified by rd field in instruction
  x0 is always 0 (writes to Reg[0]are ignored)
Program counter (PC)
  Holds address of current instruction
Memory (MEM)
  Holds both instructions & data, in one 32-bit byte-addressed memory space
  We’ll use separate memories for instructions (IMEM) and data (DMEM)
  Instructions are read (fetched) from instruction memory
  Load/store instructions access data memory
Notes:     These are placeholders for instruction and data caches

## Slide 17: Stages of the Datapath : Overview
Problem: A single, “monolithic” CL block that “executes an instruction” (performs all necessary operations beginning with fetching the instruction and completing with the register access) is be too bulky and inefficient
Solution: Break up the process of “executing an instruction” into stages, and then connect the stages to create the whole datapath
  smaller stages are easier to design
  easy to optimize (change) one stage without touching the others (modularity)

## Slide 18: Five Stages of the Datapath
Stage 1: Instruction Fetch (IF)
Stage 2: Instruction Decode (ID)
Stage 3: Execute (EX) - ALU (Arithmetic-Logic Unit)
Stage 4: Memory Access (MEM)
Stage 5: Write Back to Register (WB)

## Slide 19: Basic Phases of Instruction Execution
IMEM
+4
rs2
rs1
rd
Reg[ ]
ALU
DMEM
imm
1. Instruction
Fetch
2. Decode/
Register
Read
3. Execute
4. Memory
5. Register
Write
PC
mux
Clock
time

## Slide 20: Datapath Components: Combinational
Combinational Elements
Storage Elements + Clocking Methodology
Building Blocks
32
32
A
B
32
Sum
CarryOut
CarryIn
Adder
32
A
B
32
Y
32
Select
MUX
Multiplexer
32
32
A
B
32
Result
OP
ALU
ALU
Adder

## Slide 21: Datapath Elements: State and Sequencing (1/3)
Register
Write Enable:
  Negated (or deasserted) (0): Data Out will not change
  Asserted (1): Data Out will become Data In on positive edge of clock
clk
Data In
Write Enable
N
N
Data Out

## Slide 22: Register addressing
A memory with four words needs two address lines.
The two address inputs go through a 2 * 4 decoder to select one of the four words.
The decoder is enabled with the memory‐enable input.
Memory enable is 0 ==> all decoder outputs are 0. None of the memory words are selected.

## Slide 23: Datapath Elements: State and Sequencing (2/3)
Register file (RF) has 32 registers:
  Two 32-bit output buses: busA and busB
  One 32-bit input bus: busW
  x0 is wired to 0
Register is selected by:
  RA (number) selects the register to put on busA (data)
  RB (number) selects the register to put on busB (data)
  RW (number) selects the register to be written via busW (data) when Write Enable is 1
Clock input (clk)
  Clk input is a factor ONLY during write operation
  During read operation, behaves as a combinational logic block:
    RA or RB valid  busA or busB valid after “access time.”
Clk
busW
Write Enable
32
32
busA
32
busB
5
5
5
RW
RA
RB
32 x 32-bit
Registers

## Slide 24: Datapath Elements: State and Sequencing (3/3)
“Magic” memory
  One input bus: Data In
  One output bus: Data Out
Memory word is found by:
  For Read: Address selects the word to put on Data Out
  For Write: Set Write Enable = 1: address selects the memory word to be written via the Data In bus
Clock input (CLK)
  CLK input is a factor ONLY during write operation
  During read operation, behaves as a combinational logic block: Address valid  Data Out valid after “access time”
Clk
Data In
Write Enable
32
32
DataOut
Address

## Slide 25: Review: Complete RV32I ISA
Need datapath and control to implement these instructions

## Slide 26: Summary of RISC-V Instruction Formats
31
25
20
15
7
12
24
19
14
11
6
0
funct7
rs2
rs1
funct3
rd
opcode
30
8
21
rs1
funct3
rd
opcode
imm[11:0]
imm[11:5]
rs2
rs1
funct3
imm[4:0]
opcode
I-type
S-type
imm[12|10:5]
rs2
rs1
funct3
imm[4:1|11]
opcode
B-type
opcode
imm[31:12]
rd
U-type
R-type
opcode
imm[20|10:1|11]]
rd
imm[19:12]
J-type

## Slide 27: R-Format Instructions: Datapath
Notes: Main point here is to give you an idea of why you won’t be allowed to do certain things in design
All boil down to making sure the chip you get back behaves the way you expected
  If don’t follow the rules, fab won’t guarantee functionality

## Slide 28: Implementing the add instruction
add rd, rs1, rs2
Instruction makes two changes to machine’s state:
  Reg[rd] = Reg[rs1] + Reg[rs2]
  PC = PC + 4
0000000
rs2
rs1
000
rd
0110011
Reg-Reg OP
rd
add
add
rs2
rs1
7
5
5
3
7
5
31
25
20
15
7
12
24
19
14
11
6
0
funct7
rs2
rs1
funct3
rd
opcode

## Slide 29: Datapath for add
+4
Add
clk
addr
inst
IMEM
PC
pc+4
Inst[24:20]
ALU
+
clk
Reg [ ]
Inst[19:15]
Inst[11:7]
AddrB
AddrA
DataA
DataB
AddrD
DataD
alu
Reg[rs1]
Reg[rs2]
Inst[31:0]
Control logic
RegWriteEnable (RegWEn)
=1
add
5
5
add
Reg-Reg OP
5
31
25
20
15
7
12
24
19
14
11
6
0
0000000
rs2
rs1
000
rd
opcode
  Reg[rd] = Reg[rs1] + Reg[rs2]
  PC = PC + 4

## Slide 30: Implementing the sub instruction
sub rd, rs1, rs2
Almost the same as add, except now have to subtract operands instead of adding them
inst[30] selects between add and subtract
31
25
20
15
7
12
24
19
14
11
6
0
0000000
rs2
rs1
000
rd
0110011
0100000
rs2
rs1
000
rd
0110011
add
sub

## Slide 31: Datapath for add/sub
+4
Add
clk
addr
inst
IMEM
PC
pc+4
Inst[24:20]
ALU
+
clk
Reg [ ]
Inst[19:15]
Inst[11:7]
AddrB
AddrA
DataA
DataB
AddrD
DataD
alu
Reg[rs1]
Reg[rs2]
Control logic
RegWEn
(1=Write, 0=NoWrite)
ALUSel
(add=0/sub=1)
Inst[31:0]

## Slide 32: Implementing other R-Format instructions
All implemented by decoding funct3 and funct7 fields and selecting appropriate ALU function
0000000
rs2
rs1
000
rd
0110011
0100000
rs2
rs1
000
rd
0110011
0000000
rs2
rs1
001
rd
0110011
add
sub
sll
0000000
rs2
rs1
010
rd
0110011
slt
0000000
rs2
rs1
011
rd
0110011
0000000
rs2
rs1
100
rd
0110011
xor
0000000
rs2
rs1
101
rd
0110011
srl
0100000
rs2
rs1
101
rd
0110011
sra
0000000
rs2
rs1
110
rd
0110011
0000000
rs2
rs1
111
rd
0110011
or
and
sltu

## Slide 33: Implementing I-Format - addi instruction
RISC-V Assembly Instruction:
  addi x15,x1,-50
111111001110
00001
000
01111
0010011
OP-Imm
rd=15
add
imm=-50
rs1=1
5
3
7
5
31
20
15
7
12
19
14
11
6
0
rs1
funct3
rd
opcode
imm[11:0]
12

## Slide 34: Datapath for add/sub
+4
Add
clk
addr
inst
IMEM
PC
pc+4
Inst[24:20]
ALU
+
clk
Reg [ ]
Inst[19:15]
Inst[11:7]
AddrB
AddrA
DataA
DataB
AddrD
DataD
alu
Reg[rs1]
Reg[rs2]
Inst[31:0]
Control logic
RegWEn
(1=Write, 0=NoWrite)
ALUSel
(add=0/sub=1)
Immediate should
be here

## Slide 35: Adding addi to Datapath
+4
Add
clk
addr
inst
IMEM
PC
pc+4
Inst[24:20]
ALU
+
clk
Reg [ ]
Inst[19:15]
Inst[11:7]
AddrB
AddrA
DataA
DataB
AddrD
DataD
alu
Reg[rs1]
Reg[rs2]
Inst[31:0]
Control logic
RegWEn
(1=Write, 0=NoWrite)
ALUSel
(add=0/ sub=1)
BSel
(rs2=0/ Imm=1)
0
1
Imm[31:0]

## Slide 36: Adding addi to Datapath
+4
Add
clk
addr
inst
IMEM
PC
pc+4
Inst[24:20]
ALU
+
clk
Reg [ ]
Inst[19:15]
Inst[11:7]
AddrB
AddrA
DataA
DataB
AddrD
DataD
alu
Reg[rs1]
Reg[rs2]
Inst[31:0]
Control logic
RegWEn=1
ALUSel= add
BSel
(rs2=0/ Imm=1)
Bsel = 1
ImmSel=I
0
1
Imm[31:0]
Imm.
Gen
+4
Add
clk
addr
inst
IMEM
PC
pc+4
Inst [31:20]

## Slide 37: I-Format immediates
inst[31:0]
------inst[31]-(sign-extension)-------
inst[30:20]
imm[31:0]
Imm.
Gen
inst[31:20]
imm[31:0]
ImmSel=I
High 12 bits of instruction (inst[31:20]) copied to low 12 bits of immediate (imm[11:0])
Immediate is sign-extended by copying value of inst[31] to fill the upper 20 bits of the immediate value (imm[31:12])
-inst[31]-
31 30
20
15
7
12
19
14
11
6
0
rs1
funct3
rd
opcode
imm[11:0]
12

## Slide 38: R+I Datapath
+4
Add
clk
addr
inst
IMEM
PC
pc+4
Inst[24:20]
ALU
+
clk
Reg [ ]
Inst[19:15]
Inst[11:7]
AddrB
AddrA
DataA
DataB
AddrD
DataD
alu
Reg[rs1]
Reg[rs2]
Inst<31:0>
Control logic
RegWEn
ALUSel
BSel
0
1
Imm[31:0]
Imm.
Gen
+4
Add
clk
addr
inst
IMEM
PC
pc+4
Inst [31:20]
Works for all other I-format arithmetic instructions (slti,sltiu,andi, ori,xori,slli,srli, srai) just by changing ALUSel
ImmSel

## Slide 39: “And In conclusion…”
CPU design involves datapath and control logic
Typical five stages of exectution
We built a datapath for arithmetic and logic for RISC-V R and I instructions
  …and sketched out control
Will add data memory access (loads, stores), branches, jumps, etc…