## Slide 1: CONTROL

## Slide 2: Review
We have designed a complete datapath
  Capable of executing all RISC-V instructions in one cycle each
  Not all units (hardware) used by all instructions
5 Phases of execution
  IF, ID, EX, MEM, WB
  Not all instructions are active in all phases
Controller specifies how to execute instructions
  New instructions can be added with just control?

## Slide 3: Recap: Complete RV32I ISA
RV32I has 47 instructions
37 instructions are enough to run any C program
Not covered

## Slide 4: Complete Single-Cycle RV32I Datapath!
+4
Add
addr
inst
IMEM
pc+4
pc+4
wb
pc
wb
Inst[24:20]
ALU
+
clk
Reg [ ]
Inst[19:15]
Inst[11:7]
AddrB
AddrA
DataA
DataB
AddrD
DataD
alu
Reg[rs1]
Reg[rs2]
Inst[31:0]
Control logic
RegWEn
ALUSel
Asel
MemRW
0
1
Imm[31:0]
Imm.
Gen
Add
clk
addr
inst
IMEM
DMEM
addr
DataR
DataW
PC
Inst [31:7]
1
0
2
clk
WBSel
Branch
Comp
1
0
ImmSel
1
0
PCSel
BrUn
BrEq
BrLT
Control logic
Bsel
mem
alu
alu

## Slide 5: Register Transfer Level (RTL)
RTL describes instructions in figures or text
Can use C (or Verilog) to describe RTL
Inst Register Transfers
add R[rd]  R[rs1] + R[rs2]; PC  PC + 4
sub R[rd]  R[rs1] – R[rs2]; PC  PC + 4
ori R[rd]  R[rs1] | Imm; PC  PC + 4
jal R[rd]  PC + 4; PC  R[rs1] + Imm
beq if ( R[rs1] == R[rs2] ) PC  PC + Imm
else PC  PC + 4

## Slide 6: Our Single-Core Computer (w/o FPU, SIMD)
Processor
Control
Datapath
PC
Registers
Arithmetic & Logic Unit
(ALU)
Memory
Input
Output
Bytes
Enable?
Read/Write
Address
Write Data
ReadData
Processor-Memory Interface
I/O-Memory Interfaces
Program
Data
Cache
Processor organized around words and bytes
Memory (including
cache) organized around blocks, which are typically multiple words

## Slide 7: Single-Cycle RV32I Datapath and Control
+4
Add
addr
inst
IMEM
pc+4
pc+4
wb
Inst[24:20]
ALU
+
clk
Reg [ ]
Inst[19:15]
Inst[11:7]
AddrB
AddrA
DataA
DataB
AddrD
DataD
alu
Reg[rs1]
Reg[rs2]
Inst[31:0]
Control logic
RegWEn
ALUSel
Asel
MemRW
0
1
Imm[31:0]
Imm.
Gen
Add
clk
addr
inst
IMEM
DMEM
addr
DataR
DataW
PC
Inst [31:20]
1
0
2
clk
WBSel
Branch
Comp
1
0
ImmSel
1
0
PCSel
BrUn
BrEq
BrLT
Bsel
Control logic
mem

## Slide 8: Example: add
+4
Add
addr
inst
IMEM
pc+4
pc+4
wb
pc
wb
Inst[24:20]
ALU
+
clk
Reg [ ]
Inst[19:15]
Inst[11:7]
AddrB
AddrA
DataA
DataB
AddrD
DataD
alu
Reg[rs1]
Reg[rs2]
Inst[31:0]
Control logic
RegWEn
ALUSel
Asel
MemRW
0
1
Imm[31:0]
Imm.
Gen
Add
clk
addr
inst
IMEM
DMEM
addr
DataR
DataW
PC
Inst [31:7]
1
0
2
clk
WBSel
Branch
Comp
1
0
ImmSel
1
0
PCSel
BrUn
BrEq
BrLT
Control logic
Bsel
mem
alu
alu
7
5
5
3
7
5
31
25
20
15
7
12
24
19
14
11
6
0
funct7
rs2
rs1
funct3
rd
opcode
=pc+4
=*
=1
=*
=0
=0
=add
=Read
=1
=*
=*

## Slide 9: add Execution
1000
1004
PC
1004
1008
PC+4
add x1,x2,x3
add x6,x7,x9
inst[31:0]
Clock
Reg[2]
Reg[7]
Reg[rs1]
Reg[2]+Reg[3]
alu
Reg[7]+Reg[9]
Reg[3]
Reg[9]
Reg[rs2]
???
Reg[1]
Reg[2]+Reg[3]
+4
Add
addr
inst
IMEM
pc+4
wb
pc
wb
Inst[24:20]
ALU
+
clk
Reg [ ]
Inst[19:15]
Inst[11:7]
AddrB
AddrA
DataA
DataB
AddrD
DataD
alu
Reg[rs1]
Reg[rs2]
Inst[31:0]
Control logic
RegWEn
ALUSel
Asel
MemRW
0
1
Imm[31:0]
Imm.
Gen
Add
clk
addr
inst
IMEM
DMEM
addr
DataR
DataW
PC
Inst [31:7]
1
0
2
clk
WBSel
Branch
Comp
1
0
ImmSel
1
0
PCSel
BrUn
BrEq
BrLT
Bsel
mem
alu
alu
=pc+4
=*
=1
=*
=0
=0
=add
=Read
=1
=*
=*
Reg[2]+Reg[3]
wb
Reg[7]+Reg[9]
add control
add control
Control logic

## Slide 10: Example: sw
+4
Add
addr
inst
IMEM
pc+4
pc+4
wb
pc
wb
Inst[24:20]
ALU
+
clk
Reg [ ]
Inst[19:15]
Inst[11:7]
AddrB
AddrA
DataA
DataB
AddrD
DataD
alu
Reg[rs1]
Reg[rs2]
Inst[31:0]
Control logic
RegWEn
ALUSel
Asel
MemRW
0
1
Imm[31:0]
Imm.
Gen
Add
clk
addr
inst
IMEM
DMEM
addr
DataR
DataW
PC
Inst [31:7]
1
0
2
clk
WBSel
Branch
Comp
1
0
ImmSel
1
0
PCSel
BrUn
BrEq
BrLT
Control logic
Bsel
mem
alu
alu
=pc+4
=S
=0
=*
=1
=0
=add
=Write
=*
31
25
20
15
7
12
24
19
14
11
6
0
Imm[11:5]
rs2
rs1
funct3
imm[4:0]
opcode
offset[11:5]
base
width
src
STORE
offset[4:0]
=*
=*

## Slide 11: Example: beq
+4
Add
addr
inst
IMEM
pc+4
pc+4
wb
pc
wb
Inst[24:20]
ALU
+
clk
Reg [ ]
Inst[19:15]
Inst[11:7]
AddrB
AddrA
DataA
DataB
AddrD
DataD
alu
Reg[rs1]
Reg[rs2]
Inst[31:0]
Control logic
RegWEn
ALUSel
Asel
MemRW
0
1
Imm[31:0]
Imm.
Gen
Add
clk
addr
inst
IMEM
DMEM
addr
DataR
DataW
PC
Inst [31:7]
1
0
2
clk
WBSel
Branch
Comp
1
0
ImmSel
1
0
PCSel
BrUn
BrEq
BrLT
Control logic
Bsel
mem
alu
alu
=B
=0
=0
=1
=1
=add
=Read
=*
=*

## Slide 12: Peer Instruction(s): Critical Path (yellkey)
+4
Add
addr
inst
IMEM
pc+4
pc+4
wb
pc
wb
Inst[24:20]
ALU
+
clk
Reg [ ]
Inst[19:15]
Inst[11:7]
AddrB
AddrA
DataA
DataB
AddrD
DataD
alu
Reg[rs1]
Reg[rs2]
Inst[31:0]
Control logic
RegWEn
ALUSel
Asel
MemRW
0
1
Imm[31:0]
Imm.
Gen
Add
clk
addr
inst
IMEM
DMEM
addr
DataR
DataW
PC
Inst [31:7]
1
0
2
clk
WBSel
Branch
Comp
1
0
ImmSel
1
0
PCSel
BrUn
BrEq
BrLT
Control logic
Bsel
mem
alu
alu
Critical path for a addi
R[rd] = R[rs1]+imm
tclk-q + tAdd + tIMEM + tReg + tBComp + tALU + tDMEM + tmux + tSetup
tclk-q + tIMEM + max{tReg, tImm} + tALU + 2tmux + tSetup
tclk-q + tIMEM + max{tReg, tImm} + tALU + 3tmux + tDMEM + tSetup
None of the above

## Slide 13: Peer Instruction(s): Critical Path (citizen try)
+4
Add
addr
inst
IMEM
pc+4
pc+4
wb
pc
wb
Inst[24:20]
ALU
+
clk
Reg [ ]
Inst[19:15]
Inst[11:7]
AddrB
AddrA
DataA
DataB
AddrD
DataD
alu
Reg[rs1]
Reg[rs2]
Inst[31:0]
Control logic
RegWEn
ALUSel
Asel
MemRW
0
1
Imm[31:0]
Imm.
Gen
Add
clk
addr
inst
IMEM
DMEM
addr
DataR
DataW
PC
Inst [31:7]
1
0
2
clk
WBSel
Branch
Comp
1
0
ImmSel
1
0
PCSel
BrUn
BrEq
BrLT
Control logic
Bsel
mem
alu
alu
Critical path for a addi
R[rd] = R[rs1]+imm
tclk-q + tAdd + tIMEM + tReg + tBComp + tALU + tDMEM + tmux + tSetup
tclk-q + tIMEM + max{tReg, tImm} + tALU + 2tmux + tSetup
tclk-q + tIMEM + max{tReg, tImm} + tALU + 3tmux + tDMEM + tSetup
None of the above
tsetup

## Slide 14: Instruction Timing
IF | ID | EX | MEM | WB | Total
I-MEM | Reg Read | ALU | D-MEM | Reg W | 
200 ps | 100 ps | 200 ps | 200 ps | 100 ps | 800 ps

## Slide 15: Instruction Timing
Maximum clock frequency
  fmax = 1/800ps = 1.25 GHz
Most blocks idle most of the time
  E.g. fmax,ALU = 1/200ps = 5 GHz!
Instr | IF = 200ps | ID = 100ps | ALU = 200ps | MEM=200ps | WB = 100ps | Total
add | X | X | X |  | X | 600ps
beq | X | X | X |  |  | 500ps
jal | X | X | X |  |  | 500ps
lw | X | X | X | X | X | 800ps
sw | X | X | X | X |  | 700ps

## Slide 16: Control Logic Truth Table
CS 61c
Lecture 12: Control & Performance
Inst[31:0] | BrEq | BrLT | PCSel | ImmSel | BrUn | ASel | BSel | ALUSel | MemRW | RegWEn | WBSel
add | * | * | +4 | * | * | Reg | Reg | Add | Read | 1 | ALU
sub | * | * | +4 | * | * | Reg | Reg | Sub | Read | 1 | ALU
(R-R Op) | * | * | +4 | * | * | Reg | Reg | (Op) | Read | 1 | ALU
addi | * | * | +4 | I | * | Reg | Imm | Add | Read | 1 | ALU
lw | * | * | +4 | I | * | Reg | Imm | Add | Read | 1 | Mem
sw | * | * | +4 | S | * | Reg | Imm | Add | Write | 0 | *
beq | 0 | * | +4 | B | * | PC | Imm | Add | Read | 0 | *
beq | 1 | * | ALU | B | * | PC | Imm | Add | Read | 0 | *
bne | 0 | * | ALU | B | * | PC | Imm | Add | Read | 0 | *
bne | 1 | * | +4 | B | * | PC | Imm | Add | Read | 0 | *
blt | * | 1 | ALU | B | 0 | PC | Imm | Add | Read | 0 | *
bltu | * | 1 | ALU | B | 1 | PC | Imm | Add | Read | 0 | *
jalr | * | * | ALU | I | * | Reg | Imm | Add | Read | 1 | PC+4
jal | * | * | ALU | J | * | PC | Imm | Add | Read | 1 | PC+4
auipc | * | * | +4 | U | * | PC | Imm | Add | Read | 1 | ALU

## Slide 17: Control Realization Options
ROM
  “Read-Only Memory”
  Regular structure
  Can be easily reprogrammed
    fix errors
    add instructions
  Popular when designing control logic manually
Combinatorial Logic
  Today, chip designers use logic synthesis tools to convert truth tables to networks of gates

## Slide 18: Single-Cycle RISC-V RV32I Datapath
IMEM
ALU
Imm.
Gen
+4
DMEM
Branch Comp.
Reg[]
AddrA
AddrB
DataA
AddrD
DataB
DataD
Addr
DataW
DataR
1
0
0
1
2
1
0
pc
0
1
inst[11:7]
inst[19:15]
inst[24:20]
inst[31:7]
pc+4
alu
mem
wb
alu
pc+4
Reg[rs1]
pc
imm[31:0]
Reg[rs2]
Control Logic
inst[31:0]
ImmSel
RegWEn
BrUn
BrEq
BrLT
ASel
BSel
ALUSel
MemRW
WBSel
PCSel
wb

## Slide 19: Single-Cycle RISC-V RV32I Datapath
IMEM
ALU
Imm.
Gen
+4
DMEM
Branch Comp.
Reg[]
AddrA
AddrB
DataA
AddrD
DataB
DataD
Addr
DataW
DataR
1
0
0
1
2
1
0
pc
0
1
inst[11:7]
inst[19:15]
inst[24:20]
inst[31:7]
pc+4
alu
mem
wb
alu
pc+4
Reg[rs1]
pc
imm[31:0]
Reg[rs2]
Control Logic
inst[31:0]
ImmSel
RegWEn
BrUn
BrEq
BrLT
ASel
BSel
ALUSel
MemRW
WBSel
PCSel
wb

## Slide 20: “And In conclusion…”
We have built a processor (almost)!
  Capable of executing all RISC-V instructions in one cycle each
  Not all units (hardware) used by all instructions
  Critical path changes
5 Phases of execution
  IF, ID, EX, MEM, WB
  Not all instructions are active in all phases
Controller specifies how to execute instructions
  Implemented as ROM or logic (we’ll show you next time)